## Slide 1: SMART Home
Group 2:
John Satterla – Computer Engineer – Wireless Connectivity
Zachary Eakerns – Electrical Engineer – Biomedical Station
Zarka McClung (Team Lead) – Computer Engineer – Facial Recognition
Christian Jensen – Electrical Engineer – Voice Recognition

## Slide 2: Project Description
Our system will monitor a patient's position, and the environment around them will react to their movements. A station will be located in the home to monitor the user’s vitals including EKG, oxygen in their blood, and their heart rate. The “room” will have 2 major appliances that are activated via facial or voice recognition. Lights and other items will turn on as the user moves throughout the “room”. There will be a door that is automatically opened when the user is trying to enter the room.

## Slide 3: System Overview
John Satterla
Full size automatic door with facial recognition
Central processing Station, with Voice Recognition
Bluetooth ToF Beacon
Zigbee Module
Small Scale House Model
Biomedical Station
Microcontroller
Portable Location Detection Device
LEDs to represent Lights
Servo based washer representation
LCD screen represents TV
Computer fan to represent ceiling fan
Biomedical station gets EKG, heart rate, and blood oxygenation of the user, relays information to the Central processing station. Zigbee module takes commands from central processing station to control devices
Door can be opened automatically via facial recognition or control from central processing station via Zigbee
Central processing station (computer) displays system information and can control devices via voice commands. Communicates with rest of devices via Zigbee
Portable BLE Time of Flight device reacts to movements of user throughout the room and devices turn on inside the small scale model
Notes: Need to edit this slide to include the separate systems

## Slide 4: Controlling Devices Wirelessly with Zigbee
Zigbee is a Wireless, low power mesh networking protocol designed for home and building automation
It supports low data rates (250kbps) and works on top of the defined IEEE 802.15.4 physical layer [16]
The protocol was standardized in 2003 and is maintained by the Zigbee Alliance
Zigbee is probably in most of your homes today, with smart hubs like the Amazon Alexa or Google’s Nest able to connect all devices together
John Satterla

## Slide 5: Controlling Devices Wirelessly with Zigbee
John Satterla
[11]

## Slide 6: Controlling Devices Wirelessly with Zigbee
John Satterla
For our purposes, we will use Wireless microcontrollers that are integrated into Digi’s “Xbee” modules
[1]
[2]

## Slide 7: Controlling Devices Wirelessly with Zigbee
John Satterla
Using these so that we do not have to do any RF layout with wireless MCUs/ time constraints
Can communicate and be programmed separately for wireless purposes to form network with IDE, and then communicate back to main MCU via SPI or UART
[3]
Notes: ...

## Slide 8: Controlling Devices Wirelessly with Zigbee
John Satterla
[3]
PAN ID = Personal Area Network ID
Notes: ...

## Slide 9: Controlling Devices Wirelessly with Zigbee
John Satterla
Device Communication testing via Command Line GUI
Notes: ...

## Slide 10: Controlling Devices Wirelessly with Zigbee
John Satterla
Coordinator Sending and receiving bytes from Router w/ MSP430
MSP430 Test filling up array with received characters
Notes: ...

## Slide 11: Tracking Location of the Patient Monitor
Ideally work indoors, so using GPS not preferred because of accuracy and not able to get fix inside of buildings
BLE ToF – Bluetooth Time of Flight
  Time of Flight is used to estimate range by measuring the round trip delay of an RF packet exchange
  At least two devices needed, and operate generally as a master and a slave, where the master calculates average round trip delay for hundreds of packets to be as accurate as possible (try to reduce error from interference, other RF related differences) [ref]
John Satterla

## Slide 12: Tracking Location of the Patient Monitor
For this, Texas Instruments has a experiential stack that I am going to evaluate and see what kind of performance I can get
The tricky part will be using two masters that are positioned at two known points, and then connecting to the single slave on the patient to triangulate it’s position
[1]
John Satterla
Patient monitor
Master 1
Master 2
Notes: Show initial testing results with bluetootqh

## Slide 13: Tracking Location of the Patient Monitor
Hardware on order:
  TI CC2640R2F Launchpads
    Why an SoC? Ability to quickly sample the data coming from the slave and calculate the distance via ToF
    Specs:
      CPU: ARM Core M3 @ 48 MHz
      Memory: 128kB flash, 28kB RAM
      Radio: 2.4GHz with Certified Bluetooth 5, 4.2 support, 102 dB link budget for BLE
      Peripherals: I2C, ISS, UART, TRNG, AES-128
      Low power features: RX at 0dBm – 5.9 mA, TX at +5dBm – 9.1 mA, as low as 1.1uA standby
      General: 3.3V operation
John Satterla
Notes: Pictures, testing

## Slide 14: Biomedical Station
A station will be installed in the home that the patient can use to monitor their electrocardiogram (EKG), heart rate, and blood oxygenation.
EKG signals will be monitored using two electrodes placed on the chest as shown in the image. This information will also give heart rate.
Pulse oxygenation will be found by using a pulse oximeter that will attach to the patient's finger.

## Slide 15: Electrocardiograph
Anywhere from a 100 µV to 2 mV of voltage can be detected across the skin of a person due to heart muscles depolarizing.
This signal must be amplified by at least 500, however since the input is so small noise must be filtered out.
The primary source of noise is 60 Hz transmission lines. Due to this a notch filter will be used in addition to low pass.

## Slide 20: Measuring Blood Oxygenation
By shining a red light and an infrared light through an area on a patient containing an artery, the Sp02 level can be found by comparing the ratio of red light absorbed to infrared light absorbed.
Oxyhemoglobin absorbs more infrared light, while deoxyhemoglobin absorbs more red light.
[5]
[5]

## Slide 21: Pulse Oximetry Calculations
As mentioned, the oxygenation of a person's blood is found by using the ratio of light absorbed.
Found using the equation
Where

## Slide 22
[5]

## Slide 24: Software
Peak detection and accurate readings from an ADC are the main tasks of the biomedical station's program.
An MSP430G2553 will be used in order to conserve on both the projects budget and power consumption.
The G2553 has a 10-bit ADC which with the low voltage of the project will be sensitive up to 0.1 mV.

## Slide 25: Moving Forward
Amplifiers must be acquired and tested before being integrated with filters.
Code will continue to be written. For EKG the values from the ADC must be graphed in real-time, while an algorithm needs to be written to control the LED's and calculate pulse oxygenation.
Once these are finished the two will be integrated allowing a laptop to display the patient's vitals.

## Slide 26: Voice Recognition Methods
Matlab [7]
  Using the computer and its microphone to detect voice
    Allows for easier integration with the entire project
    Using the Voicebox Toolbox [9]
    Contains many voice and audio related functions
Process:
Ask user to set up phrases before
  Type name of phrase
  Speak the phrase (3x times)
  Find the PSD of the signal
  Set peaks as template
Speech recognition
  Poll for incoming phrases
  Sample input
  Find the PSD of the signal
  Compare peaks with Template
*The system will be speaker dependent
(Only recognizing one specific person's commands)

## Slide 28: VoiceRecording.m

## Slide 29: VoiceReader.m

## Slide 30: Voice Recognition – Noise Filtering
Objective:
  Isolate users' speech from background noise
Method:
  Adaptive filter[13]
    Requires noise data – noise.wav
    Still working through example code*
Least Mean Squared adaptive filter

## Slide 31
Face Recognition Using OpenCV v3.4 and Python v2.7
This Photo by Unknown Author is licensed under CC BY-ND
This Photo by Unknown Author is licensed under CC BY-NC
This Photo by Unknown Author is licensed under CC BY-ND
Goal: Detect recognized user’s face to open a door automatically.

## Slide 32
Face Recognition Using OpenCV v3.4 and Python v2.7
Why use OpenCV computer vision library?
Free-to-use open source computer vision and machine learning software library (BSD license - minimal to no restrictions on the use of the library)
Can employ the code and tweak it as we want by adding copyright notice
Can access more than 2,500 algorithms using the library
Guided tutorials and documentation available

## Slide 33
Phases of Face Recognition and Automatic Door

## Slide 34
Turning on webcam
Using Frontal face harcascade classifier
getting ID number
Collecting 21 samples and getting out of the loop
[3]
[11]

## Slide 36
Recognizer = LBPH (LOCAL BINARY PATTERNS HISTOGRAMS) Face Recognizer, included with OpenCV package
Join root path with image name to create list of all images
Converting PIL (python image library) images to gray scale & numpy array format
Converting integer array to numpy array for Ids

## Slide 37
Provides a complete histogram and now we have trained the software using our userIDs

## Slide 38: Plan for Phase III and IV
Phase III:
  Code Recognizer
  Use the .yml file generated to detect ID1 vs ID2
  Use recognizer.predict to predict the userID and also display the confidence of prediction
  Also display Unknown for unauthorized users
Phase IV:
  Use prediction to send serial communication to a microprocessor
  Turn on a stepper motor if the user is authenticated.
  Inform main system which userID left/ entered the house.

## Slide 39: Power Budget
Part Name | Quantity | Supply Voltage (V) | Supply Current (mA) | Power Subtotal (W)
Lenovo E545 laptop | 1 | 20 | 3250 | 65
MSI GT72VR Laptop | 1 | 19.5 | 11800 | 230
MSP430G2553 | 2 | 2.2 | 0.23 | 1 m
LM324 | 2 | 5 | 1 | 10 m
AD624 | 1 | 9 | 5 | 45 m
LED | 2 | 2 | 18 | 36 m
Phototransistor | 1 | 0.8 | 2 | 1.6 m

## Slide 40: Gantt Chart

## Slide 41: Gantt Chart

## Slide 42: Budget

## Slide 43: Material Cost

## Slide 44: References
“DIGI XBEE® AND DIGI XBEE-PRO® ZIGBEE,” digi.com, 2018. [Online]. Available: https://www.digi.com/pdf/ds_xbee_zigbee.pdf. [Accessed: 25-Sep-2018].
“EM351/EM357 High-Performance, Integrated ZigBee/802.15.4 System-on-Chip,” silabs.com, 2013. [Online]. Available: https://www.silabs.com/documents/public/data-sheets/EM35x.pdf. [Accessed: 25-Sep-2018].
“Face Recognition Using OpenCV,” The Codacus, 23-Jun-2017. [Online]. Available: https://thecodacus.com/face-recognition-loading-recognizer/#.W72PXGhKjIU. [Accessed: 10-Oct-2018].
“Filter Audio Signal Using MATLAB Code,” Reconstructing an Image from Projection Data - MATLAB & Simulink Example. [Online]. Available: https://www.mathworks.com/help/simulink/ug/tutorial-integrating-matlab-code-with-a-simulink-model-for-filtering-an-audio-signal.html#bsdakyu-3. [Accessed: 10-Oct-2018].]:
“How pulse oximeters work explained simply.,” How Equipment Works. [Online]. Available: https://www.howequipmentworks.com/pulse_oximeter/. [Accessed: 18-Sep-2018].
How to Design Peripheral Oxygen Saturation (SpO2) and Optical Heart Rate Monitoring (OHRM) Systems Using the AFE4403, 3AD. [Online]. Available: http://www.ti.com/lit/an/slaa655/slaa655.pdf. [Accessed: 20-Sep-2018].
“Least mean squares filter,” Wikipedia, 16-Aug-2018. [Online]. Available: https://en.wikipedia.org/wiki/Least_mean_squares_filter. [Accessed: 10-Oct-2018].
M. Brooks, “VOICEBOX: Speech Processing Toolbox for MATLAB,” Description of fxpefac. [Online]. Available: http://www.ee.ic.ac.uk/hp/staff/dmb/voicebox/voicebox.html#sigproc. [Accessed: 10-Oct-2018].]
“OpenCV library,” About - OpenCV library. [Online]. Available: https://opencv.org/. [Accessed: 10-Oct-2018].
“OpenCV Reviews: Overview, Pricing and Features,” Financesonline.com. [Online]. Available: https://reviews.financesonline.com/p/opencv/. [Accessed: 10-Oct-2018].
“OpenCV: Core functionality,” Cascade Classification - OpenCV 2.4.13.7 documentation. [Online]. Available: https://docs.opencv.org/3.4/d0/de1/group__core.html#ga0f9314ea6e35f99bb23f29567fc16e11. [Accessed: 10-Oct-2018].
“Zigbee | Overview | Wireless Connectivity,” SimpleLinkTM Zigbee Wireless MCUs, 2018. [Online]. Available: http://www.ti.com/wireless-connectivity/simplelink-solutions/zigbee/overview.html. [Accessed: 26-Sep-2018].

## Slide 45: Questions?