## Slide 1: SMART Home
Group 2:
John Satterla – Computer Engineer – Wireless Connectivity
Zachary Eakerns – Electrical Engineer – Biomedical Station
Zarka McClung – Computer Engineer – Facial Recognition
Christian Jensen [Team Lead] – Electrical Engineer – Voice Recognition

## Slide 2: Project Description
Our system will monitor a patient's position, and the environment around them will react to their movements. A station will be located in the home to monitor and display the user’s electrocardiogram . The “room” will have 2 major appliances that are activated via facial or voice recognition. Lights and other items will turn on as the user moves throughout the “room”. There will be a door that is automatically opened when the user is trying to enter the room.​

## Slide 3: Responsibilities
John
Location detection
Wireless communication with Zigbee
Graphical user interface
Device control/interfacing in model house Zarka
Christian
Voice recognition
PCB desig Zach
EKG circuitry
Biomedical Station
Model House Construction
Facial Recognition
Serial Communication
Stepper Motor for door

## Slide 4: Safety
Always wear appropriate PPE
Careful of short circuits, set current limits on power supplies when testing circuits
Make sure to have common ground

## Slide 5: System Overview
John Satterla
Full size automatic door with facial recognition
Central processing Station, with Voice Recognition
Bluetooth ToF Beacon
Zigbee Module
Small Scale House Model
Biomedical Station
MSP430 Microcontroller
Portable Location Detection Device
LEDs to represent Lights
Stepper motor to represent washer
LCD screen represents TV
Computer fan to represent ceiling fan
Biomedical station gets EKG, heart rate, and blood oxygenation of the user, relays information to the Central processing station via Bluetooth.
Door can be opened automatically via facial recognition or control from central processing station via Zigbee
Central processing station (computer) displays system information, EKG readings, and can control devices via voice commands. Communicates with rest of devices via Zigbee
Portable BLE Time of Flight device reacts to movements of user throughout the room and devices turn on inside the small scale model
Bluetooth Communication
PCB controls model’s devices

## Slide 6: Smart Home Communication via Zigbee
Zigbee
  Chosen because not sending much data other than characters to control devices (Zigbee data rate is 250kbps), Bluetooth would be overkill and not accomplish a true “mesh network”
  Mesh networking allows for devices other than the coordinator (plugged into main computer) to join and leave the network, without problems thanks to automatic routing configuration built into the Zigbee specification
  Long range – XBee modules from Digi support ranges up to 100m line of sight
Zigbee Network Example Topology [14]

## Slide 7: Smart Home Communication via Zigbee
XBee Modules from Digi
  Uses Silicon Labs EM357 Zigbee SoC from Silicon Labs
  Run Zigbee Pro 2007 (current spec is 3.0)
  Communicate with two MSP430’s on green-board via UART, with computer via UART with RS-232 adapter
[2]
[4]

## Slide 8: Location Monitoring of Patient
Bluetooth Time of Flight Program run on 2 TI CC2640R2F LaunchPads
  Specs of CC2640R2F:
    32-bit ARM Cortex M3 @ 48-MHz
    28kB SRAM
    128kB flash
    PCB antenna on LaunchPad
[13]

## Slide 9: Location Monitoring of Patient
Bluetooth Time of Flight program sends packets from ‘initiator’ to the ‘responder’ and measures the time and RSSI (received signal strength indication) for each packet, then estimates the distance between the initiator and the responder
[1]

## Slide 10: Location Monitoring of Patient
Bluetooth Time of Flight program sends packets from ‘initiator’ to the ‘responder’ and measures the time and RSSI (received signal strength indication) for each packet, then estimates the difference distance the initiator and the responder
Raw ToF output

## Slide 11: Location Monitoring of Patient – Post Processing
Accuracy of ToF
  Calibration has to occur each time the program starts, with each LaunchPad 1 meter away
  Within 1-2m for each ToF measurement taken, giving me the 3-4m intervals for each “room”
Post distance processing algorithm in Python:
  1. Take each measurement and place into an array of 10 measurements (first in, first out), call this measurementArray
  2. Take the average of the measurementArray
  3. Add this average to another array of 10 previous averages called averageArray, also (first in, first out)
  4. Take the average of the last 10 averages (basically last 100 measurements taken)
  5. Send the averaged value to the checkLocation function

## Slide 12: Location Detection – Processing in Python

## Slide 13: Graphical User Interface
Using Python 3, with TkInter as GUI, and pyserial for communication to USB dongle with XBee module and CC2640R2F LaunchPad
Added logging so we can debug somewhere other than the command line, and logging will also be useful for users
Logging to aid debugging
Current GUI for Control and monitoring of devices

## Slide 14: Devices – Model House Schematic

## Slide 15: Devices – Model House Schematic
10uF caps help reduce noise on input and improve high frequency load regulation on output[11]

## Slide 16: Devices – Model House Schematic
87K pulldown on gate of BS170 so pin doesn’t float
PWM for fan on P2.1 (Timer A1 on MSP430)

## Slide 17: MSP430 Device Control Code
MSP #1
MSP #2

## Slide 18: Model House with Devices
LEDs #1 - #4
Fan
Washer

## Slide 19: GUI and Location Detection Program Demos
https://youtu.be/dGLGNG8CIQU – GUI manual control
https://youtu.be/VugtU7GQIsI- Location Detection
Notes: https://youtu.be/ESfKke6Pie4

## Slide 20: EKG Monitoring
Voltages ranging from 100 µV to 2 mV can be found across the chest due to the heart depolarizing and repolarizing
By amplifying and filtering these signals, an electrocardiogram can be made
By utilizing Python this data can be graphed and displayed in real time

## Slide 21: EKG Circuit Simulation

## Slide 22: EKG Circuit Simulation Continued

## Slide 24: Code Composer Studio Code
Needed to control the MSP430G2553 microcontroller
This microcontroller was used for its ADC that would allow the voltages from the circuit to be graphed
The ADC10 allowed for a distinction of approximately 3 mV

## Slide 26: Python Code
Was used to graph data from ADC in real time
Used serial communication through Bluetooth with the aid of the BlueSMiRF chip

## Slide 27: Results
Without artifact
With artifact

## Slide 28
Zachary Eakerns

## Slide 29: Video of EKG
https://www.youtube.com/watch?v=uSn0SAEYFiA

## Slide 30
Zachary Eakerns

## Slide 31
Zachary Eakerns

## Slide 32: Voice Recognition
Done in Matlab
Using one outside toolbox – VoiceBox [7]
  Using the []=melceps() function
    Returns the cepstrum vector of the signal time vectors
Single user
  Requires prerecording of specific phrases for detection

## Slide 39
Phrase String Table example

## Slide 41
Demo Screen Recording of Recognition
https://youtu.be/yX46B4Bykhw

## Slide 42: Green Board Design
2 MSP paired with an XBee Module
  2x MSP430G IC
  3x regulators
    All REG1117 adjustable LDOs [1]
      1 A output (max)
      3.3V,5V,12V
  XBee Module on header pins
  Design done in Eagle Cad

## Slide 45
Face Recognition Using OpenCV v3.4 and Python v2.7
This Photo by Unknown Author is licensed under CC BY-ND
This Photo by Unknown Author is licensed under CC BY-NC
This Photo by Unknown Author is licensed under CC BY-ND
Goal: Detect recognized user’s face to open a door automatically.

## Slide 46
Face Recognition Using OpenCV v3.4 and Python v2.7
Why use OpenCV computer vision library?
Free-to-use open source computer vision and machine learning software library (BSD license - minimal to no restrictions on the use of the library)
Can employ the code and tweak it as we want by adding copyright notice
Can access more than 2,500 algorithms using the library
Guided tutorials and documentation available
[8]
[9]

## Slide 47
Phases of Face Recognition and Automatic Door

## Slide 48: How different features are detected?
Each feature of the user is obtained by subtracting sum of pixels under the white rectangle from sum of pixels under black rectangle. For example, user’s nose area will have lighter shade compared to the eye area. So, the Haar feature uses black edges around the eyes, compared to white edges around the nose. [3]
To have minimum error, Haar features are added to all training images, which means more capture of user images will lead to least error and accurate classification.

## Slide 49
[5]
[10]
Turning on webcam
Using Frontal face harcascade classifier
getting ID number
Collecting 1000 samples and getting out of the loop
Assigning ID # to images

## Slide 51: Training the Recognizer
LBP pattern histogram [Rosebrock, A.]
Each pixel of grayscale image is selected with its neighboring pixel surrounding the center pixel. Then a local binary pattern is generated for this center pixel and stored in the output 2D array [12]
This method is used on all captured images to train the recognizer and stored in a trainingData.yml file.
[12]

## Slide 52
Recognizer = LBPH (LOCAL BINARY PATTERNS HISTOGRAMS) Face Recognizer, included with OpenCV package
Join root path with image name to create list of all images
Converting PIL (python image library) images to gray scale & numpy array format
Converting integer array to numpy array for Ids
[5]

## Slide 53
Provides a complete histogram and now we have trained the software using our userIDs

## Slide 54: Recognition and Sending Serial Command
Importing trained yml file
Sending char “A” to open the door when authorized user is detected
Setting up COM port to send signal to Zigbee module
Setting high acceptance range for confidence level (0 = perfect match)
[5]​

## Slide 55: Stepper motor door setup
NEMA 17 SM-42BYG011-25 stepper motor

## Slide 56: Setting up variables and defining functions
To send signal door is closed
Using 16MHz clock

## Slide 57: MSP430 motor code
Authorized user detected
Take enough steps to open the door
Close the door
Send feedback to central monitoring system door is closed
STEP -Logic Output. Triggers the motor to step forward one step.
DIR -Logic Output. Determines the direction of motor rotation.

## Slide 58: Link of working facial recognition
https://www.youtube.com/watch?v=9QVIsDHt_aM

## Slide 59: Power Budget
Part Name | Quantity | Supply Voltage (V) | Supply Current (mA) | Power Subtotal (W)
Lenovo E545 laptop | 1 | 20 | 3250 | 65
MSI GT72VR Laptop | 1 | 19.5 | 11800 | 230
MSP430G2553 | 2 | 3.3 | 0.42 | 1.4m
BlueSMiRF | 1 | 3.3 | 4 | 13.2 m
AD624 | 1 | 6 | 5 | 30 m
NEMA 17 stepper motor | 1 | 7.5 | 330 | 2.475

## Slide 60: Gantt Chart

## Slide 61: Gantt Chart

## Slide 62: Budget

## Slide 63: Material Cost

## Slide 64: References
Dev.ti.com. (2018). Localization Toolbox — SimpleLink™ CC2640R2 BLE-Stack User's Guide for *Bluetooth®* 4.2 3.02.00.00 documentation. [online] Available at: http://dev.ti.com/tirex/content/simplelink_cc2640r2_sdk_2_20_00_49/docs/blestack/ble_user_guide/html/localization/index.html [Accessed 3 Oct. 2018].
DIGI XBEE® AND DIGI XBEE-PRO® ZIGBEE,” digi.com, 2018. [Online]. Available: https://www.digi.com/pdf/ds_xbee_zigbee.pdf. [Accessed: 25-Sep-2018].
Docs.opencv.org. (2018). OpenCV: Face Detection using Haar Cascades. [online] Available at: https://docs.opencv.org/3.4/d7/d8b/tutorial_py_face_detection.html [Accessed 26 Sep. 2018].
“EM351/EM357 High-Performance, Integrated ZigBee/802.15.4 System-on-Chip,” silabs.com, 2013. [Online]. Available: https://www.silabs.com/documents/public/data-sheets/EM35x.pdf. [Accessed: 25-Sep-2018].
“Face Recognition Using OpenCV,” The Codacus, 23-Jun-2017. [Online]. Available: https://thecodacus.com/face-recognition-loading-recognizer/#.W72PXGhKjIU. [Accessed: 10-Oct-2018].
K, T. (2018). Easy Driver Hook-up Guide. [online] Available at: https://learn.sparkfun.com/tutorials/easy-driver-hook-up-guide [Accessed 14 Nov. 2018].
M. Brooks, “VOICEBOX: Speech Processing Toolbox for MATLAB,” Description of fxpefac. [Online]. Available: http://www.ee.ic.ac.uk/hp/staff/dmb/voicebox/voicebox.html#sigproc. [Accessed: 10-Oct-2018].]
“OpenCV library,” About - OpenCV library. [Online]. Available: https://opencv.org/. [Accessed: 10-Oct-2018].
“OpenCV Reviews: Overview, Pricing and Features,” Financesonline.com. [Online]. Available: https://reviews.financesonline.com/p/opencv/. [Accessed: 10-Oct-2018].
“OpenCV: Core functionality,” Cascade Classification - OpenCV 2.4.13.7 documentation. [Online]. Available: https://docs.opencv.org/3.4/d0/de1/group__core.html#ga0f9314ea6e35f99bb23f29567fc16e11. [Accessed: 10-Oct-2018].
“REG1117A (ACTIVE),” REG1117A 1A Low Dropout Positive Regulator | TI.com. [Online]. Available: http://www.ti.com/product/REG1117A. [Accessed: 07-Nov-2018].
Rosebrock, A. (2018). Local Binary Patterns with Python & OpenCV - PyImageSearch. [online] PyImageSearch. Available at: https://www.pyimagesearch.com/2015/12/07/local-binary-patterns-with-python-opencv/ [Accessed 24 Oct. 2018].
“SimpleLink Bluetooth® low energy CC2640R2F wireless MCU LaunchPad development kit,” LM741 Operational Amplifier | TI.com. [Online]. Available: http://www.ti.com/tool/LAUNCHXL-CC2640R2. [Accessed: 05-Dec-2018].
Zigbee Network Example Topology [“Zigbee | Overview | Wireless Connectivity,” SimpleLinkTM Zigbee Wireless MCUs, 2018. [Online]. Available: http://www.ti.com/wireless-connectivity/simplelink-solutions/zigbee/overview.html. [Accessed: 26-Sep-2018].

## Slide 65: Questions?

## Slide 66: All videos
https://youtu.be/dGLGNG8CIQU – GUI manual control
https://youtu.be/VugtU7GQIsI - Location Detection
https://www.youtube.com/watch?v=uSn0SAEYFiA – EKG
Demo Screen Recording of Recognition – MatLAB voice recog.
https://www.youtube.com/watch?v=9QVIsDHt_aM – facial recog.