## Slide 1: SMART Home
Group 2:
John Satterla – Computer Engineer – Wireless Connectivity
Zachary Eakerns [Team Lead] – Electrical Engineer – Biomedical Station
Zarka McClung – Computer Engineer – Facial Recognition
Christian Jensen – Electrical Engineer – Voice Recognition

## Slide 2: Last Week's Deliverables
Have working location tracking
Determine all Zigbee protocol commands
Begin integrating and building out GUI
Zachary Eakerns
John Satterla
Christian Jensen
Zarka McClung
Have python graphing the ADC in real time
Make headway on circuit instability
Finish green board design
Continue writing Matlab code for voice recognition
-25tor SM-42BYG011-25
Write Python code to send serial communication to Zigbee
Establish motor code upon signal from Zigbee co-ordinator
-25tor SM-42BYG011-25

## Slide 3: Graphical User Interface – Updates and Control of Devices
Added sliders for LED’s that are on and off only, Fan has 4 speeds including off. Each slider is dynamic (reacts to network), for instance if the location tracking turns on an LED the slider will reflect that. (program on next slides)
Need to work on controlling computer fan w/ MSP (will need transistor circuit), and work on interfacing LCD and servo. Would like to include some type of temperature detection for automatic fan control

## Slide 4: Graphical User Interface – More Development
Using Python 3, with tkinter as GUI, and pyserial for communication to USB dongle with Xbee module

## Slide 5: Graphical User Interface – Early Development
Using Python 3, with tkinter as GUI, and pyserial for communication to USB dongle with Xbee module

## Slide 6: Updates on Location Detection
TI got back to me, they had me change the setting I was using.
Now, instead of using the “Auto ToF” mode, using “Connected ToF”
  Connected ToF allows for more packets to be sent at a higher rate, therefore increasing accuracy
  TI tells me that this is designed for specifically ToF applications, while Auto was designed to interleave with a standard Bluetooth Connection
  Tell me that antenna’s should be facing each other and calibration at 1m is extremely important
  Increasing the syncwords (what I tried last week) was making the RAM overflow because of how much was being stored while sending and receiving the additional packets. Each syncword added adds 8 bytes of RAM usage on both the initiator and receiver
Results are MUCH improved. Fewer negatives and connection is maintained across much longer distances
  Examples on next slide
  Will tinker with adding syncwords to see if accuracy is improved without overloading RAM
Deliverables for next week
  Spit out info over UART
  Improve accuracy further and characterize it

## Slide 7: Updates on Location Detection
@ 3m

## Slide 8: Updates on Location Detection
@2m

## Slide 9: Updates on Location Detection
@ 6m

## Slide 10: Progress on Code
The definition function in Python code was unreachable, causing error
To fix this, the line makeFig() was added telling python to enter the definition

## Slide 11: Code Debugging
The information send to the BlueSMiRF from the MSP is not correct, causing the BlueSMiRF to output undefined characters which Python cannot interpret
Further debugging will be done to fix this error, which could be due to the MSP's buffer size, or a mismatch in actual baud rate

## Slide 12: Circuitry
Without heavy artifact
With heavy artifact

## Slide 17
Least Mean Squared adaptive filter

## Slide 20: Green Board Design
2 MSP paired with an XBee Module
  2x MSP430G IC
  3x regulators
    All REG1117 adjustable LDOs [1]
      1 A output (max)
      3.3V,5V,12V
  XBee Module on header pins
  Design done in Eagle Cad

## Slide 21: Update
Was able to establish serial communication using XBee module
When authorized user is detected "door open" is send to COM8 port
When unknown user is detected "door close" is send to COM8 port
COM8 port is set as my coordinator module which will pass this information to Router module (connected to motor to open door)
Modified face detector code to implement these changes
Next week's plan
NEMA 17 SM-42BYG011-25 bipolar stepper motor will be used to open the door
Will be coding to detect RX pin of Router module to send signal to the stepper motor

## Slide 22: Door open

## Slide 23: Door close

## Slide 24: Opening door concept
Motor on one side with a string attached to a nail
Stepper Motor

## Slide 25: Gantt Chart

## Slide 26: Gantt Chart

## Slide 27: Budget

## Slide 28: Material Cost

## Slide 29: Next Week's Deliverables
Start integrating GUI's
Start interfacing devices
Improve accuracy of location detection
Zachary Eakerns
John Satterla
Christian Jensen
Zarka McClung
Have python graphing the ADC in real time
Finalize code for MATLAB serial communication
Order green board
Establish motor code upon signal from Zigbee coordinator

## Slide 30: References
“REG1117A (ACTIVE),” REG1117A 1A Low Dropout Positive Regulator | TI.com. [Online]. Available: http://www.ti.com/product/REG1117A. [Accessed: 07-Nov-2018].

## Slide 31: Questions?