## Slide 1: SMART Home
Group 2:
John Satterla – Computer Engineer – Wireless Connectivity
Zachary Eakerns – Electrical Engineer – Biomedical Station
Zarka McClung – Computer Engineer – Facial Recognition
Christian Jensen [Team Lead] – Electrical Engineer – Voice Recognition

## Slide 2: Last Week's Deliverables
Start integrating GUI's
Start interfacing devices
Improve accuracy of location detection
Zachary Eakerns
John Satterla
Christian Jensen
Zarka McClung
Have python graphing the ADC in real time
Make headway on circuit instability
Finish green board design
Continue writing Matlab code for voice recognition
Write Python code to send serial communication to Zigbee
Establish motor code

## Slide 3: Graphical User Interface – More Development
Using Python 3, with TkInter as GUI, and pyserial for communication to USB dongle with XBee module
Added logging so we can debug somewhere other than the command line, and logging will also be useful for users
Log for yesterday, creates a new log for each day
Current GUI for Control and monitoring of devices

## Slide 4: Graphical User Interface – Demo
GUI allows control and can receive updates (for instance if door is trigger by facial recognition, or voice recognition receives command)
Notes: https://www.youtube.com/watch?v=b2MJs8F0EOw&feature=youtu.be

## Slide 5: Location Detection
TI got back to me, they had me change the setting I was using.
Now, instead of using the “Auto ToF” mode, using “Connected ToF”
  Connected ToF allows for more packets to be sent at a higher rate, therefore increasing accuracy
  TI tells me that this is designed for specifically ToF applications, while Auto was designed to interleave with a standard Bluetooth Connection
  Tell me that antenna’s should be facing each other and calibration at 1m is extremely important
  Increasing the syncwords (what I tried last week) was making the RAM overflow because of how much was being stored while sending and receiving the additional packets. Each syncword added adds 8 bytes of RAM usage on both the initiator and receiver
Results are MUCH improved. Fewer negatives and connection is maintained across much longer distances
  Examples on next slide
  Will tinker with adding syncwords to see if accuracy is improved without overloading RAM

## Slide 6: Location Detection – Processing in Python
Currently able to reliably distinguish between 0-3m, 3-6m, and 6-10m. This would be good, but want to increase accuracy by testing in environment where demoing (basement hallway probably)
Actual accuracy of ToF
  Calibration has to occur each time the program starts, with each LaunchPad 1 meter away
  Within 1-2m for each ToF measurement taken, giving me the 3-4m intervals for each “room”
Current processing algorithm in Python:
  1. Take each measurement and place into an array of 10 measurements (first in, first out), call this measurementArray
  2. Take the average of the measurementArray
  3. Add this average to another array of 10 previous averages called averageArray, also (first in, first out)
  4. Take the average of the last 10 averages (basically last 100 measurements taken)
  5. Send the averaged value to the checkLocation function

## Slide 7: Location Detection – Processing in Python

## Slide 8: Location Detection – Integrated with GUI and Zigbee Networking
Notes: https://www.youtube.com/watch?v=ADMcdPN37zU

## Slide 9: MSP off Launchpad Testing - Schematic

## Slide 10: MSP off Launchpad Testing - LM317AT
TI LM317AT Adjustable Regulator
  1% output Voltage accuracy LDO
  Maximum input-output voltage differential: -0.3 – 40 V
  Current limit for TO-220 (Vin- Vout < 15 V : 1.5 - 3.4 A
  For 3.3 V output:
    Closest resistor to 393Ω was 385 Ω, recommended value from TI for R1 is 240 Ω
  C1 needed to filter out noise on input
  C2 optional, improves transient response

## Slide 11: MSP off Launchpad Testing - LM317AT
TI LM317AT Adjustable Regulator
  1% output Voltage accuracy LDO
  Maximum input-output voltage differential: -0.3 – 40 V
  Current limit for TO-220 (Vin- Vout < 15 V : 1.5 - 3.4 A
  For 3.3 V output:
    Closest resistor to 393Ω was 385 Ω, recommended value from TI for R1 is 240 Ω
  C1 needed to filter out noise on input
  C2 optional, improves transient response
Within 1% error and no detectable ripple

## Slide 12: MSP off Launchpad Testing - Schematic
  Nothing too interesting here, 47K pullup resistor used on
  RX and TX of XBee and MSP connections

## Slide 13: MSP off Launchpad Testing - Video
Simple Echo program from XBee command line
Notes: https://www.youtube.com/watch?v=3BMpv4auUMM

## Slide 14: Python Code
The definition function in Python code was unreachable, causing error
To fix this, the line makeFig() was added telling python to enter the definition

## Slide 15: Python Code Continued
Encode function was causing error each time code was run
Removing this allowed for the graph to work

## Slide 16: Code Composer Studio Code
Bloated due to many changes, revisions, and commented out sections
Made code more difficult to read and debug
The bulk of the error is likely to happen in this program, so a clean and readable version was needed

## Slide 19: Circuitry
Without artifact
With artifact

## Slide 24: Green Board Design
2 MSP paired with an XBee Module
  2x MSP430G IC
  3x regulators
    All REG1117 adjustable LDOs [1]
      1 A output (max)
      3.3V,5V,12V
  XBee Module on header pins
  Design done in Eagle Cad

## Slide 26: Code changes
Ser.write -> sends one char
Need a delay to send all characters "open"/"close"
Plan is to assign A = door open B= door close

## Slide 27: Door open

## Slide 28: Door close

## Slide 29: NEMA 17 SM-42BYG011-25 stepper motor
Current needed for easy driver:
2A (max)
Voltage needed:
6V – 30V
Around 200 steps for 1 rev
[2]

## Slide 30: MSP430G2553 with Stepper
Connection setup
A == Green
A_N == Red
B == Blue
B_N == Yellow
STEP -Logic Input. Triggers the motor to step forward one step.
DIR -Logic Input. Determines the direction of motor rotation.

## Slide 31: Gantt Chart

## Slide 32: Gantt Chart

## Slide 33: Budget

## Slide 34: Material Cost

## Slide 35: Next Week's Deliverables
Zachary Eakerns
John Satterla
Christian Jensen
Zarka McClung
House built
All circuitry off breadboard and integrated with code to display EKG graph in real time
Finalize code for MATLAB serial communication
Order green board
Code TX/RX of MSP
Finalize motor code upon signal from Zigbee coordinator
Get OLED display and computer fan integrated with MSP
Integrate GUI fully, and add an option to turn off ToF and turn in back on

## Slide 36: References
“REG1117A (ACTIVE),” REG1117A 1A Low Dropout Positive Regulator | TI.com. [Online]. Available: http://www.ti.com/product/REG1117A. [Accessed: 07-Nov-2018].
K, T. (2018). Easy Driver Hook-up Guide. [online] Available at: https://learn.sparkfun.com/tutorials/easy-driver-hook-up-guide [Accessed 14 Nov. 2018].

## Slide 37: Questions?